# INCF Task Force
# Standard Language in Neural Network Models
# Ivan Raikov
Okinawa Institute of Science and Technology
          raikov (at) oist (dot) jp
## Abstraction Layer Interface Description
## Introduction
A computer language is defined by its syntax and semantics. The syntax describes the form of language and is most conveniently done using a grammar specification to facilitate parser development. The semantics define the meaning of the sentences that can be constructed given the syntax of the language.
NineML targets the formal and portable description of large-scale neuronal networks. Its definition is divided in a descriptive (or user) layer, and an abstraction layer. The abstraction layer starts with description of elementary concepts such as state machines and common mathematical expressions. The user layer builds on these elementary concepts to provide a library of common model types to user applications. The user layer provides a convenient syntax to express customary idioms of large-scale networks in computational neuroscience. Its semantics are conceptual but all the mathematical details and execution policies of the models are rigoroulsy defined by the abstraction layer.
This paper introduces a number of fundamental building blocks for the abstraction layer, that allow to:
1. express simple mathematical expressions including functions and differential equations.
2. Express state switching mechanisms based on external information.
3. group mathematical expressions and state full mechanisms

We note that in the context of simulation paradigms the first two points can possibly understood as execution policies, replacing the need of turing completeness (fi for and while loops), while the third point allows to structure a model. It should also be clear that there are implicit assumptions: one cannot create groups without firs tselecting the elements of the group (so this introduces the notions of both set abstractions and element selections).

Based on these primitive building blocks, the abstraction layer can then define

neurons
synapses
constructiive gouprs
connections

and make these types available as a library to the user layer.

 The goal of the working group proposal should be to provide the starting point for the Stockholm meeting, which will focus on the definition of the abstraction layer. The work group may use the following guiding questions to develop their design:
What is the object model necessary to represent the operation of the elements described in the user layer?
What are the interfaces necessary to plug together the different parts of the model (e.g. how to describe a network where each neuron is given parameters based on its physical location, or other network properties)?
How are state update rules represented?
Equation representation
Handling of discrete spiking events
Initialization/model constructors
How are constructive groups represented?
  1. Representation of physical space
  2. Representation of feature spaces
  3. Distance functions
Probability distributions
  1. How would a new extension to the user layer be implemented? (Subclassing, setting properties, etc)
  2. What is the mechanism for extending existing classes?
  3. What is the mechanism for adding new classes?
  4. What is the mechanism for adding qualitatively new structures
(e.g. SBML reactions)
Notations used in this document
We use both a graphical notation and a textual notation to develop the example models in this document. The meaning of the elements of both notations is explained when they are introduced below.

Fundamentals: Components and their Signatures
In the following sections we try to construct an userlayer type IaF for a (leaky) integrate and fire neuron.
The membrane potential of a leaky integrate and fire neuron is calculated using a degenerate cable equation. We say that this equation is a component of the type IaF and the membrane potential is a variable (of the component and the type). Components are depicted in a box in the graphical notation, variables are omitted or present as the label of an edge:

[IaF]

Textually this can be conveniently expressed as:

An integrate and fire neuron model can emit spikes and pass them to other neurons. A spike is generated when the membrane potential crosses a threshold. For sake of simplicity we assume here that the thresholding mechanism has a variable that has the value 1 when the membrane potential is greater that (or equal to) the threshold, and that has the value of 0 when the membrane potential is lower than the treshold (see below for a useful extension to this representation).

[Thr}

Connecting these components gives:

Variables

Grouping

Informal Semantics
We propose to structure the parts of a model by means of components and signatures, which are analogous to classes and interfaces in object-oriented languages. The difference is that while a class in an object-oriented introduces a single new type, a component can introduce as many new types as it wants, as well as functions that act on those types. A structure can enforce data representation abstraction in a way that is more general than data hiding in object oriented programming. For example, suppose that the model interface is defined with the following signature:

  (signature Model

     (component SN: SpikingNode)
     (component SY: Synapse)
     (component CG: ConstructiveGroup)
     (component CN:  Connection)
   )

### Spiking Nodes
We propose to describe spiking nodes by means of diagrams that describe the relationships between continuous dynamics, events, and state transitions.

A spiking node is defined by a set of quantities that evolve continuously with time, according to a set of rules such as a system of ordinary differential equations. A change in the dynamics of such a quantity can be due to a change in the continuous environment or due to a discrete event. Additionally, the spiking node definition may contain parameters, which are quantities held constant during integration.

The dynamics of a spiking node can be represented as signal flow diagrams, which consist of signal nodes and arrows. A signal node is the representation of a continuous function that takes one or more signal values as input (specified by input arrows), and returns one or more signal values (specified by output arrows).

For example, the following diagram represents an ordinary differential equation:

In this case, the arrows labels only identify the names of the input and output quantities; a more detailed representation may also contain information identifying states and parameters:

As a further extension of the diagram notation, we will introduce the notion of combinator node, which is an object that can encapsulate one or more subgraphs with special properties. For example, let us define the SWITCH combinator to represent regime change of a hybrid dynamical system:

The SWITCH combinator enacpsulates two subgraphs. Each of the two subgraphs represents a dynamical system. The output signal is the output signal of the first of the systems, unless an event has occurred, in which case the output of the combinator is the output of the second system. The input set to the combinator is the union of the inputs to the two encapsulated subgraphs, plus a transition event signal.

RSWITCH is the recurring variant of SWITCH, which performs a switch when from the first system to the second system when event e1 occurs, and back to the first system when event e2 occurs.
An Example
Based on the notation described above, here is an example of a simple integrate-and-fire description:

TODO: Insert Hugo's graph as an example here.

Let us then adopt the following definition for the SpikingNode signature:

  (signature SpikingNode
     (type state)
     (type parameters)
     (signal-nodes  :: SignalNode list)
     (signal-arrows :: state * parameters -> SignalArrow list)
     (initial-state :: state)
   )
where
1. (type state): a representation of the state vector of the spiking system
2. (type parameters): a representation of the parameter set of the spiking system
3. (signal-arrows :: state * parameters -> SignalArrow list): a function that takes in as argument a state vector and parameter set, and returns the corresponding signal flow diagram
4. (initial-state :: state): initial state vector

### Synapses
### Constructive Groups
The ConstructiveGroup signature can then be defined as follows:

  (signature ConstructiveGroup
     (type prototype)
     (type space)
     (construct :: space * prototype -> group)
   )
where
1. (type prototype): the type of prototype nodes
2. (type space): the type of the topological space (structure) of the constructive group
3. (construct :: space * prototype -> group): the constructor function of the constructive group

In the definition above, type group is a generic representation of group topology and can be e.g. a set, multiset, or a group-based data field. For sets, each element in the set is neighbor of any other element (a set can be reordered arbitrarily). For multisets, each element is also neighbor of any other, however, the elements are not required to be distinct as in a set). Group-based data fields (GBF) are an extension of the notion of array, where the elements are indexed by the elements of a group, called the shape of the GBF (see Giavitto and Michel, 2001). A GBF value associates values to some indices of a shape. This kind of collection can be used to describe uniform and regular topologies like: n-ary trees, n-dimensional grids, circular grids, etc. For example, the following definition

   gbf Grid2D = < X, Y >
introduces a new two-dimensional shape called Grid2D, corresponding to a classical 2D grid (a cell above, below, left or right, but not diagonal). The two names, X and Y refer to the directions that can be followed to reach the neighbors of an element.

### Connections
The Connection signature can then be defined as follows:

  (signature Connection
     (construct :: group * group -> graph)
   )